ELEC 7770-001, Spring 2007

Homework # 3

Assigned: Monday, Apr. 2, 2007

# Due: Tuesday, Apr. 17, 2007

Problem 1: A clock signal is routed to two edge-triggered flip-flops A and B that form a two-bit shift register. The following circuit is extracted from the layout. Find clock skews for the two flip-flops.

Problem 2: Given that the setup time is 3ps and hold time is 5ps for each flip-flop, design the two-bit shift register satisfying the short-path and long path constraints. Find a lower bound on the clock period for your design.

Problem 3: How will you reroute the clock signal to improve the design? Note that a design that is better than the zero-skew design is possible.

# Text boxes

FF B

FF A

Clock

source

C2 = 0.725pF

C1 = 0.725pF

R2 = 10Ω

1 = 5Ω

R1 = 5Ω