04-25-2008                                                                              Mohammed Ashfaq Shukoor

Advanced VLSI Design Project

a. This example is for 4-bit unsigned integer multiplication

| Count | Step | Multiplicand | Product |
| --- | --- | --- | --- |
| 0 | Initial values | 0010 | 0000 0011 |
| 1 | LSB=1 => Prod=Prod+Mcand | 0010 | 0010 0011 |
|  | Right shift product | 0010 | 0001 0001 |
| 2 | LSB=1 => Prod=Prod+Mcand | 0010 | 0011 0001 |
|  | Right shift product | 0010 | 0001 1000 |
| 3 | LSB=0 => no operation | 0010 | 0001 1000 |
|  | Right shift product | 0010 | 0000 1100 |
| 4 | LSB=0 => no operation | 0010 | 0000 1100 |
|  | Right shift product | 0010 | 0000 0110 |

State Diagram of Multiplier Control Unit

b. Design and Verification:

The circuit was encoded in VHDL and was verified using a test bench.

Snippets of the Simulation Listing:

| Test |  | ns | delta | Clk | Reset | Start | Multiplier (decimal) | Multiplicand (decimal) | Product (decimal) | Done |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1. | Initial | 40 | +1 | 1 | 0 | 1 | 4294967295 | 4294967295 | 0 | 0 |
|  | Final | 2000 | +1 | 1 | 0 | 0 | 4294967295 | 4294967295 | 18446744065119617025 | 1 |
| 2. | Initial | 2200 | +1 | 1 | 0 | 1 | 1000003 | 10009 | 0 | 0 |
|  | Final | 3720 | +1 | 1 | 0 | 0 | 1000003 | 10009 | 10009030027 | 1 |
| 3. | Initial | 4400 | +1 | 1 | 0 | 1 | 4027531843 | 2013275929 | 0 | 0 |
|  | Final | 6000 | +1 | 1 | 0 | 1 | 4027531843 | 2013275929 | 8108532912792907147 | 1 |

c. 32-bit Multiplier:

Synthesized using Leonardo Spectrum with 0.35 micron tsmc technology

| Circuit Statistics |
| --- |
| # of Inputs | 67 |
| # of Outputs | 65 |
| Critical Path Delay | 12.90 ns |
| Clock Frequency | 75 MHz |
| # of combinational gates | 634 |
| # of FFs | 109 |
| total # of gates | 1236 |

Component Listing obtained from Leonardo:

Cell       Library  References     Total Area

and03       tsmc035_typ     1 x      2      2 gates

ao32        tsmc035_typ     1 x      2      2 gates

aoi21       tsmc035_typ     4 x      1      5 gates

aoi22       tsmc035_typ    30 x      1     44 gates

aoi222      tsmc035_typ    32 x      2     72 gates

aoi32       tsmc035_typ     1 x      2      2 gates

buf02       tsmc035_typ     5 x      1      5 gates

dff         tsmc035_typ     8 x      5     38 gates

dffr        tsmc035_typ   101 x      6    564 gates

inv01       tsmc035_typ    69 x      1     52 gates

inv02       tsmc035_typ    43 x      1     33 gates

mux21_ni    tsmc035_typ    67 x      2    121 gates

nand02      tsmc035_typ    36 x      1     36 gates

nand03      tsmc035_typ     4 x      1      5 gates

nand04      tsmc035_typ     4 x      1      6 gates

nor02_2x    tsmc035_typ     1 x      1      1 gates

nor02ii     tsmc035_typ     9 x      1     11 gates

nor03_2x    tsmc035_typ     1 x      1      1 gates

nor04       tsmc035_typ     1 x      1      1 gates

oai21       tsmc035_typ    41 x      1     51 gates

oai22       tsmc035_typ    31 x      1     46 gates

oai32       tsmc035_typ     1 x      2      2 gates

or02        tsmc035_typ     3 x      1      4 gates

or03        tsmc035_typ     1 x      2      2 gates

or04        tsmc035_typ     1 x      2      2 gates

xnor2       tsmc035_typ    32 x      2     61 gates

xor2        tsmc035_typ    32 x      2     68 gates

Number of ports :                     132

Number of nets :                      663

Number of instances :                 560

Number of references to this view :     0

Total accumulated area :

Number of gates :                    1236

Number of accumulated instances :     560

d. Sequential ATPG:

*****Fault List Statistics*****

Fault Class              Uncollapsed   Collapsed

Full (FU)                       4590        3112

Det_simulation (DS)             4257        2806

Posdet (PD)		                38          24

Unused (UU)                      146         146

Redundant (RE)                     4           4

Atpg_untestable (AU)              19          19

Unobserved (UO)                  124         111

Uncontrolled (UC)                  2           2

Fault coverage                93.16%      90.55%

Test coverage                 96.31%      95.14%

ATPG effectiveness            97.04%      96.10%

*****Test Patterns Statistics*****

Total Test Cycles Generated = 371

Total Test Cycles Simulated = 1747

User CPU Time   : 1333.8 seconds

System CPU Time : 3.1 seconds

Fault Classes:

Untestable Faults:

Untestable (UT) faults are faults for which no pattern can exist to either detect or possible detect them. Untestable faults cannot cause functional failures, so the tool excludes them when calculating test coverage. These consist of the following subclasses,

1. Unused Faults (UU):

The unused fault class includes all faults on circuitry unconnected to any circuit observation point. For example the faults on the Qbar lines of FFs.

2. Redundant (RE):

The redundant fault class includes faults the test generator considers undetectable. After failing to generate any test for these faults the, the pattern generator performs a special analysis to verify that these faults are undetectable under any conditions.

Testsbale Faults:

These faults are those which cannot be proven untestable. The testable class contains the following subclasses:

1. Detected Faults(DS):

These are the faults for which tests have been found by the ATPG tool.

2. Posdet (PD):

The posdet (possible-detected) fault class includes all faults that fault simulation identifies as possible-detected but not hard detected. A possible-detected fault results from a 0-X or 1-X difference at an observation point.

3. ATPG_untestable (AU):

The ATPG untestable fault class includes all faults for which the test generator is unable to find a pattern to create a test, and yet cannot prove the fault redundant. Testable faults are put under this category if no test is found due to constraints in the ATPG tool.

Example: In the multiplier circuit the faults on the Clock line connected to the counter where placed under this category.

1     AU    /ctrl_unit_count_2_/CLK

0     AU    /ctrl_unit_count_2_/CLK

1     AU    /ctrl_unit_count_3_/CLK

0     AU    /ctrl_unit_count_3_/CLK

4. Undetected (UD):

The undetected fault class includes undetected faults that cannot be proven untestable or

ATPG_untestable. The undetected class contains two subclasses:

- uncontrolled (UC) – faults which can never be activated during pattern simulation, i.e. they are uncontrollable.

Example: In the multiplier circuit the sa0 on the ‘Done’ line was placed under this category.

- unobserved (UO) - faults whose effects do not propagate to an observable point.

e. 32-bit Multiplier with Full Scan:

The Full Scan Design was implemented using the DFTAdvisor tool from Mentor Graphics

| Circuit Statistics |
| --- |
| # of Inputs | 69 |
| # of Outputs | 65 |
| Critical Path Delay | 12.82 ns |
| Clock Frequency | 74.4 MHz |
| # of combinational gates | 634 |
| # of FFs | 109 |
| Total # of gates | 1378 |

Component Listing:

Cell       Library  References     Total Area

and03       tsmc035_typ     1 x      2      2 gates

ao32        tsmc035_typ     1 x      2      2 gates

aoi21       tsmc035_typ     4 x      1      5 gates

aoi22       tsmc035_typ    30 x      1     44 gates

aoi222      tsmc035_typ    32 x      2     72 gates

aoi32       tsmc035_typ     1 x      2      2 gates

buf02       tsmc035_typ     5 x      1      5 gates

inv01       tsmc035_typ    69 x      1     52 gates

inv02       tsmc035_typ    43 x      1     33 gates

mux21_ni    tsmc035_typ    67 x      2    121 gates

nand02      tsmc035_typ    36 x      1     36 gates

nand03      tsmc035_typ     4 x      1      5 gates

nand04      tsmc035_typ     4 x      1      6 gates

nor02_2x    tsmc035_typ     1 x      1      1 gates

nor02ii     tsmc035_typ     9 x      1     11 gates

nor03_2x    tsmc035_typ     1 x      1      1 gates

nor04       tsmc035_typ     1 x      1      1 gates

oai21       tsmc035_typ    41 x      1     51 gates

oai22       tsmc035_typ    31 x      1     46 gates

oai32       tsmc035_typ     1 x      2      2 gates

or02        tsmc035_typ     3 x      1      4 gates

or03        tsmc035_typ     1 x      2      2 gates

or04        tsmc035_typ     1 x      2      2 gates

sff         tsmc035_typ     8 x      6     49 gates

sffr_ni     tsmc035_typ   101 x      7    695 gates

xnor2       tsmc035_typ    32 x      2     61 gates

xor2        tsmc035_typ    32 x      2     68 gates

Number of ports :                     134

Number of nets :                      703

Number of instances :                 560

Number of references to this view :     0

Total accumulated area :

Number of gates :                    1378

Number of accumulated instances :     560

Test Generation:

The test generation for the Full Scan design was done using FastScan from Mentor Graphics. The following is the statistics report

ATPG Statistics report

-------------------------------------------

#faults   #faults

fault class               (coll.)   (total)

-----------------------   -------   -------

FU (full)                   3480      5030

-----------------------   -------   -------

DS (detected)               3397      4946

UU (unused)                   70        70

RE (redundant)                 4         4

AU (atpg_untestable)           9        10

-----------------------   -------   -------

test_coverage              99.74%    99.80%

fault_coverage             97.61%    98.33%

atpg_effectiveness        100.00%   100.00%

-------------------------------------------

#test_patterns                          62

#simulated_patterns                     96

CPU_time (secs)                       15.5

-------------------------------------------

Fault Classes:

Unused Faults, Redundant Faults and the ATPG untestable faults have the same meaning as described in the previous section.

Scan Test Cycles:

Of the 62 vectors generated for the circuit, the first vector is for the testing the scan chain. It consists of alternating pairs of 0s and 1s. Hence,

ncomb = # of combinational test vectors = 61

nsff = # of scan FFs

Thus, Scan test cycles = (ncomb + 2) 109 + ncomb + 4

= (61 + 2) 109 + 61 + 4

= 6932 clock cycles

Gate Overhead Calculation:

Gate Overhead = [4 nsff / (ng + 10 nff)] x 100%

Where,

ng = # of combinational gates = 634

nff = # of FFs = 109

nsff = # of scan FFs = nff =109

Estimated Gate Overhead = [(4 x 109) / (ng + (10 x 109))] x 100%

= 25.29%

Actual Gate Overhead = [(1378 – 1236) / 1236] x 100%

=11.49%

# Text boxes

Regload=’1’

Shiftreg=’1’

Regload=’1’

Mcandload = ‘1’

Done =’1’

LSB =’0’ AND Count < 32

LSB =’1’ AND Count < 32

Count = 32

Start =’1’

Start = ’0’

INIT

Check

RShift

Add

HALT